## Slide 1: APPLICATION FOR APPLYING CORRECTORS WITH COUPLED ERROR TO TOLERANCE ANALYSIS
American Society for Precision Engineering
Precision Machine Design Topical Conference
Tyler Seawright
M.S. Mechanical Engineering
July 15, 2025

## Slide 2: Error Budgets and Why they are Feared
“Budget” is associated with scarcity and stress
Budgets can be difficult to organize and manage
Often requires advanced modeling of a complex system
Notes: Error budgets are one of the last requests the typical engineer wants to hear, but why?
Budget is associated with the stress of deciding what to do with a scarce resource
Without a good budget, systems don’t operate as intended whether it is tracking calories, planning monthly finances, or developing a precision machine.
We look to the GUM for guidance on error budgets

## Slide 3: Error Budget Definitions
Chart: 
| Mary | Sue | Timothy | Dylan | Anthony | Janet
Pie | 15 | 5 | 5 | 25 | 15 | 20
Each person gets a portion of the pie, but all must agree on how to divide it
After a lengthy debate and negotiation, it was determined Dylan needs ¼ for a gym bulk and Sue and Timothy only want a taste since they prefer cake.
Image credit to pngall.com
Notes: After addressing why each person needed specific quantities, the allocation of the pie can be determined.
Error budgets apportion total error to identified sources to drive design decisions
Good error budgets identify the sources the system is most sensitive to such as Dylan, who needs to maintain a daily calorie intake and consumes the largest portion of the pie.

## Slide 4: Generalized Error Analysis with Coupled Motion
Geometric error types often include coupled error on other axes such as Abbe error.
3D error stacks including coupled error are the most general, yet can be challenging to model, manage, and validate.
Simple 2D case modeled with a rotation propagated across a unit distance.
z
y
x
y
z
x
(X,Y) Displacement
Notes: Coupled error propagates through stacks of parts
3D stacks are challenging to model when considering stacking abbe error
In this 2D case, you could use trigonometry to solve in your head, but moving to 3D or to multiple parts becomes more challenging

## Slide 5: Application Overview
Design tool that solves error from a tolerance stack in 3D.
Runs directly in Excel as a macro requiring no programming
Macro calls precompiled MATLAB code (Open-Source on GitHub)
Uses HTM to propagate error through a system of transforms
Includes input to apply correctors and propagate coupled errors associated with using them.
Notes: u + Nsigma analysis provides a realistic distribution of many built systems because what is “worst case” when you have many parts assembled? RSS works for 1D, but not well for 3D so Montecarlo is used.
App is an excel macro running an executable written in Matlab.
Does not require Matlab to use and does not require programming. Matlab source code and Macro are open sourced.
Errors are propagated using HTM

## Slide 6
Application UI
Run TolStack
Nominal Vectors
Local Errors
Corrector Definition
Montecarlo Setup
Exported Result
Excel Button
Notes: UI is Excel
Formatting flexible, but information must be tagged
Freedom to build Excel as you wish
Highlight data and hit run button to calculate
Figures and results placed in Excel

## Slide 7: Error Model by HTM
A transform path is defined by multiplying 4x4 HTMs.
Applying error terms to each transform solves the absolute error transform.
Eq. 3 solves relative difference between the two, representing error in this analysis.
(eq. 1)
(eq. 2)
(eq. 3)
Notes: Transform path is defined by 4x4 HTMs multiplied together
Error terms at each transform solve absolute error transform
Eq. 3 solves the relative difference between two transforms

## Slide 8: Error Corrector Definition
Corrector is a device that corrects an error in a system with respect to a coordinate system.
A corrector is defined with a 1x6 vector as the minimum adjustable resolution on each axis and a 1x6 vector as the position and orientation with respect to the adjusted point of interest
Tip/Tilt Adjuster Credit Newport SN100C-F2K
Tip
Tilt
Origin
POI
Notes: A corrector is a device that corrects an error such as an adjuster or actively controlled device.
A corrector is defined by minimum adjustable resolution and origin in 6 axes with respect to the corrected object.
Often, the corrector origin is not located at the point of interest (POI) to be corrected.

## Slide 9: Error Correcting by HTM
Start
Solve
Generate Corrector Difference Vector and HTM when
Generate HTM to Corrector Origin from POI
Solve Absolute Error with Corrector at POI
Solve Relative Error with Corrector at POI and Convert to Vector
Solution:
Notes: Do not spend much time on this slide, it is explained in the paper
This flowchart outlines how the difference between errored position and corrected position is solved and the corrector is applied at a distance of POI to corrector origin.
HTM() represents MATLAB functions to convert vectors to and from HTM’s
Example on next slide

## Slide 10: Model Validation 1
17mrad error corrected to 2.5mrad with corrector located at Origin
Vector Name | X | Y | Z |  |  | 
Rae | 0.9999 | 0.0170 | 0 | 0 | 0 | 0.0170
Re | -0.0001 | 0.0170 | 0 | 0 | 0 | 0.0170
Rce | 0 | 0.0025 | 0 | 0 | 0 | 0.0025
Vector Name | X | Y | Z |  |  | 
Rae | 0.9999 | 0.0170 | 0 | 0 | 0 | 0.0170
Re | -0.0001 | 0.0170 | 0 | 0 | 0 | 0.0170
Rce | 0 | 0.0025 | 0 | 0 | 0 | 0.0025
z
y
x
y
z
x
Rcae
Rae
Y Error
Error
1un
Correction
1un
Notes: 17mrad theta z error is corrected by a corrector with rotation axis at the origin
Across a unit length, such as a meter, 17mrad error results in 17mm error.
Correcting for rotation to the resolution of the adjuster, the position error is reduced with the angle error.

## Slide 11: Model Validation 2
Vector Name | X | Y | Z |  |  | 
Rae | 0.9999 | 0.0170 | 0 | 0 | 0 | 0.0170
Re | -0.0001 | 0.0170 | 0 | 0 | 0 | 0.0170
Rce | -0.0000 | 0.0310 | 0 | 0 | 0 | 0.0025
Vector Name | X | Y | Z |  |  | 
Rae | 0.9999 | 0.0170 | 0 | 0 | 0 | 0.0170
Re | -0.0001 | 0.0170 | 0 | 0 | 0 | 0.0170
Rce | -0.0000 | 0.0310 | 0 | 0 | 0 | 0.0025
17mrad error corrected to 2.5mrad with corrector located 1 unit from POI
z
y
x
y
z
x
Rcae
Rae
Y Error
Error
z
y
x
Correction
1un
1un
Y Error INCREASES when using Corrector
1un
1un
POI
Notes: In this example the corrector axis is moved and introduces an additional position error in Y as a result of correcting angle.
Since the corrector is placed 1 unit away in the opposite direction, correcting angle increases error in Y

## Slide 12: Application: Telescope Objective
Task: Determine if the focusing optics of this telescope can be assembled with respect to mechanical datums using mechanical tolerances or require alignment.
Focusing Optics
Aberration Correction Optics
Eyepiece Imaging Optics
Ray Trace
Assembly Dimensions
Notes: Walk through example
Fictional telescope objective has two mirrors and a pinhole.
Dimensions are given and tolerances added in Excel.
Task, determine if the focusing optics can be assembled with respect to the mechanical datums of the assembly fixed or require alignment before bonding.

## Slide 13: Telescope Objective Requirements
Requirement | Value | Unit
Uncertainty must be within ±N-sigma distribution | 3 | -
First and Second Mirror, and Pinhole Centration wrt mechanical datums (x,y,z) | 0.08 0.08 0.08 | mm mm mm
First and Second Mirror Orientation wrt mechanical datums (Tx, Ty, Tz) | 1.7 1.7 25 | mrad mrad mrad
Ray Trace
Assembly Dimensions
Notes: All uncertainties must be within a ±3-sigma distribution or 6-sigma distribution range.
Requirements are 80um position on all three optics and orientations for the mirrors with Z-orientation loose for axially symmetric mirrors.

## Slide 14: System Error Model
3 transform paths from each optic center to mechanical datums.
Each feature has tolerances
Notes: The error model starts with defining the transform path between coordinate systems.
Three transform paths modeled by vectors from the mechanical datum of the subassembly to each optic are created and input into Excel with local tolerances.

## Slide 15: Fixed Optic Model Outputs
Requirements not met
Notes: Mu + Nsigma requirements not met, concern areas circled in red
No correctors used.
Correctors needed on all circled in red if tolerances are not changed.

## Slide 16: Fixed Optic Model Output Histograms
CS0CS1
CS0CS2
CS0CS3
Notes: Distributions are normal

## Slide 17: Aligned Optic Model Outputs
Requirements met
Correctors Used
Notes: Mu + Nsigma uncertainty requirements met
Correctors used on pinhole and 2nd mirror

## Slide 18: Aligned Optic Model Output Histograms
CS0CS1
CS0CS2
CS0CS3
Notes: Corrected axis distributions tighten as standard deviation goes to zero and average approaches corrector resolution

## Slide 19: Conclusion
Script is a powerful addition to the ME’s toolbox for rapid tolerance analysis and determination of required corrector axes and ranges
Script is open sourced and may be plugged into custom analyses in MATLAB, however, functions well for studies completely built in Excel for non-programmers.
Systems of high complexity may be modeled with a few bridges in Excel called the “Math Model”
Notes: Powerful addition to ME toolbox without needing to code
Open sourced and modular enough to create custom analysis
Bridge connections between subsystems in Excel

## Slide 20: Future Work
Embed macro into Excel and pre-compile MATLAB script
Add sensitivity input option for non-mechanical error analysis
Add ability to change input error distribution types
Add code smarts to suggest corrector range and resolution when given requirements.
Add code smart to use corrector as ± centered at zero instead of always +
Notes: Complete tool with Excel Macro to eliminate all coding. Solve only highlighted region of spreadsheet.
Enable sensitivity inputs
Enable custom error input distributions
Enable code to suggest corrector range and res when given requirements
Enable code to pick corrector direction (nit picky but more generalized)