## Slide 1
APPLICATION FOR APPLYING CORRECTORS WITH COUPLED ERROR TO TOLERANCE ANALYSIS
APPLICATION WORKFLOW IN EXCEL
Input data with tagged rows for each input.
Verify the nominal path with Check Path.
Output results with Solve.
FIGURE 1. The TolStack application is 2 buttons that read from and write to the highlighted cells in an active Excel spreadsheet without any setup or install.
Tyler Seawright
M.S. Mechanical Engineering
ERROR CORRECTOR COUPLING AND PROPAGATION
TolStack output error histograms and error values indicating correctors are needed.
Nominal Vectors
Local Errors
Correctors
MC Config
Result
TolStack App UI
Nominal Transform
Tip
Tilt
Origin
POI
SAMPLE APPLICATION: OPTIC ALIGNMENT
Start
Solve
Generate Corrector Difference Vector and HTM when
Generate HTM to Corrector Origin from POI
Solve Absolute Error with Corrector at POI
Solve Relative Error with Corrector at POI and Convert to Vector
Solution:
FIGURE 2. Corrector parasitic error is propagated to the system using the corrector difference transform solved by the process in the flowchart.
1m
ERROR PROPAGATION BY HOMOGENEOUS TRANSFORMS
Compute absolute and relative error between the global reference and point of interest.
(eq. 1)
(eq. 2)
(eq. 3)
MODEL VALIDATION 1
A corrector at the origin corrects to the resolution of the adjuster with crosstalk.
z
y
x
y
z
x
Y Error
Error
1m
Correction
Vector Name | X (m) | Y (m) | Z (m) |  |  | 
Rae | 0.9999 | 0.0170 | 0 | 0 | 0 | 0.0170
Re | -0.0001 | 0.0170 | 0 | 0 | 0 | 0.0170
Rce | 0 | 0.0025 | 0 | 0 | 0 | 0.0025
Vector Name | X (m) | Y (m) | Z (m) |  |  | 
Rae | 0.9999 | 0.0170 | 0 | 0 | 0 | 0.0170
Re | -0.0001 | 0.0170 | 0 | 0 | 0 | 0.0170
Rce | 0 | 0.0025 | 0 | 0 | 0 | 0.0025
FIGURE 3. A 17mrad error is corrected to 2.5mrad with the corrector located at the origin.
MODEL VALIDATION 2
Vector Name | X (m) | Y (m) | Z (m) |  |  | 
Rae | 0.9999 | 0.0170 | 0 | 0 | 0 | 0.0170
Re | -0.0001 | 0.0170 | 0 | 0 | 0 | 0.0170
Rce | -0.0004 | 0.0310 | 0 | 0 | 0 | 0.0025
Vector Name | X (m) | Y (m) | Z (m) |  |  | 
Rae | 0.9999 | 0.0170 | 0 | 0 | 0 | 0.0170
Re | -0.0001 | 0.0170 | 0 | 0 | 0 | 0.0170
Rce | -0.0004 | 0.0310 | 0 | 0 | 0 | 0.0025
z
y
x
y
z
x
Rcae
Rae
Y Error
Error
z
y
x
Correction
1m
1m
1m
1m
POI
Ray Trace
Transform Path
Task: Determine if the focusing optics of this telescope can be assembled with respect to mechanical datums using mechanical tolerances or require alignment.
CS0CS1
CS0CS2
CS0CS3
Requirements not met
Correctors Needed
FIGURE 5. Sample optical system under evaluation.
FIGURE 6. Without any correction or adjusters, the requirements are not met so correctors are required to align the optics.
CS0CS1
CS0CS2
CS0CS3
Requirements met
Correctors Used
FIGURE 7. Using correctors, the requirements are met and decreased the standard deviation shown by width of the distributions.
Using correctors, the error is reduced but not eliminated entirely due to coupled motion.
2025 Joint Committee for Guides in Metrology. Evaluation of measurement data – Guide to the expression of uncertainty in measurement. 2008.
T. A. Seawright, TolStack V1.0 [Computer Software]. 2025. https://github.com/TylerSeawright/TolStack
A. H. Slocum, Precision Machine Design. Prentice-Hall, Inc., 1992.
Duenner, Andrew C. An Error Budgeting Framework for Engineering Design. Massachusetts Institute of Technology. 2019.
REFERENCES
ERROR CORRECTOR DEFINITION
An error corrector is a device used to correct an error with respect to a reference.
FIGURE 4. A 17mrad error is corrected to 2.5mrad and adds error in Y direction.

## Slide 2
APPLICATION FOR APPLYING CORRECTORS WITH COUPLED ERROR TO TOLERANCE ANALYSIS
APPLICATION WORKFLOW IN EXCEL
Input data with tagged rows for each input.
Verify the nominal path with Check Path.
Output results with Solve.
FIGURE 1. The TolStack application is 2 buttons that read from and write to the highlighted cells in an active Excel spreadsheet without any setup or install.
Tyler Seawright
M.S. Mechanical Engineering
ERROR CORRECTOR COUPLING AND PROPAGATION
TolStack output error histograms and error values indicating correctors are needed.
Nominal Vectors
Local Errors
Correctors
MC Config
Result
TolStack App UI
Nominal Transform
SAMPLE APPLICATION: OPTIC ALIGNMENT
Start
Solve
Generate Corrector Difference Vector and HTM when
Generate HTM to Corrector Origin from POI
Solve Absolute Error with Corrector at POI
Solve Relative Error with Corrector at POI and Convert to Vector
Solution:
FIGURE 2. Corrector parasitic error is propagated to the system using the corrector difference transform solved by the process in the flowchart.
1m
ERROR PROPAGATION BY HOMOGENEOUS TRANSFORMS
Compute absolute and relative error between the global reference and point of interest.
(eq. 1)
(eq. 2)
(eq. 3)
MODEL VALIDATION 1
A corrector at the origin corrects to the resolution of the adjuster with crosstalk.
z
y
x
y
z
x
Y Error
Error
1m
Correction
Vector Name | X (m) | Y (m) | Z (m) |  |  | 
Rae | 0.9999 | 0.0170 | 0 | 0 | 0 | 0.0170
Re | -0.0001 | 0.0170 | 0 | 0 | 0 | 0.0170
Rce | 0 | 0.0025 | 0 | 0 | 0 | 0.0025
Vector Name | X (m) | Y (m) | Z (m) |  |  | 
Rae | 0.9999 | 0.0170 | 0 | 0 | 0 | 0.0170
Re | -0.0001 | 0.0170 | 0 | 0 | 0 | 0.0170
Rce | 0 | 0.0025 | 0 | 0 | 0 | 0.0025
FIGURE 3. A 17mrad error is corrected to 2.5mrad with the corrector located at the origin.
MODEL VALIDATION 2
Vector Name | X (m) | Y (m) | Z (m) |  |  | 
Rae | 0.9999 | 0.0170 | 0 | 0 | 0 | 0.0170
Re | -0.0001 | 0.0170 | 0 | 0 | 0 | 0.0170
Rce | -0.0004 | 0.0310 | 0 | 0 | 0 | 0.0025
Vector Name | X (m) | Y (m) | Z (m) |  |  | 
Rae | 0.9999 | 0.0170 | 0 | 0 | 0 | 0.0170
Re | -0.0001 | 0.0170 | 0 | 0 | 0 | 0.0170
Rce | -0.0004 | 0.0310 | 0 | 0 | 0 | 0.0025
z
y
x
y
z
x
Rcae
Rae
Y Error
Error
z
y
x
Correction
1m
1m
1m
1m
POI
Ray Trace
Transform Path
Task: Determine if the focusing optics of this telescope can be assembled with respect to mechanical datums using mechanical tolerances or require alignment.
CS0CS1
CS0CS2
CS0CS3
Requirements not met
Correctors Needed
FIGURE 5. Sample optical system under evaluation.
FIGURE 6. Without any correction or adjusters, the requirements are not met so correctors are required to align the optics.
CS0CS1
CS0CS2
CS0CS3
Requirements met
Correctors Used
FIGURE 7. Using correctors, the requirements are met and decreased the standard deviation shown by width of the distributions.
Using correctors, the error is reduced but not eliminated entirely due to coupled motion.
Tip
Tilt
Origin
POI
ERROR CORRECTOR DEFINITION
An error corrector is a device used to correct an error with respect to a reference.
2025 Joint Committee for Guides in Metrology. Evaluation of measurement data – Guide to the expression of uncertainty in measurement. 2008.
T. A. Seawright, TolStack V1.0 [Computer Software]. 2025. https://github.com/TylerSeawright/TolStack
A. H. Slocum, Precision Machine Design. Prentice-Hall, Inc., 1992.
Duenner, Andrew C. An Error Budgeting Framework for Engineering Design. Massachusetts Institute of Technology. 2019.
REFERENCES
A corrector not located at the origin adds translational error through coupled motion while reducing error on the rotation Z axis.
FIGURE 4. A 17mrad error is corrected to 2.5mrad and adds error in Y direction.

## Slide 3
Nominal Vectors
Local Errors
Correctors
MC Config
Result
TolStack App UI
Nominal Transform

## Slide 4
z
y
x
y
z
x
Rcae
Rae
Y Error
Error
z
y
x
Correction
1m
1m
1m
1m
POI
Re_CS0_CS1
Re_CS0_CS2
Re_CS0_CS3

## Slide 5
CS0CS1
CS0CS2
CS0CS3
Requirements met
Correctors Used